## Slide 1: HDR-Nets 2020 MoGAN: GAN based Next PoA Selection for Proactive Mobility Management
Boyun Jang
boyunj0226@skku.edu
Dept. of Artificial Intelligence
Sungkyunkwan University, Korea
13th October 2020

## Slide 2: Overview
Problem Statement
Deep Learning Approaches for Prediction
MoGAN
Evaluations
Conclusions

## Slide 3: Problem Statement
Requirement
  Sub 10ms mobility delay for 5G
Problem
  User assisted reactive mobility management in 4G is potential bottleneck for 5G
Solution
  Proactive mobility management
3/21

## Slide 4: Problem Statement
Requirements of proactive mobility management
  Next Point of Attachment (PoA) prediction with high accuracy
  Optimal decision for handover trigger time
Challenges
  Dense and Ultra-dense cell deployment in 5G
  Real-time prediction and decision algorithms
Solution
  This work focuses on prediction of next PoA
  A GAN based next PoA prediction mechanism
4/21

## Slide 5: DL Approaches for Prediction
5/21
Recurrent Neural Network (RNN)
  Pros: Available to capture the feature of continuous data
  Cons: Gradient vanishing problem occurs with long sequence length Long-term dependency
Long Short-Term Memory (LSTM)
  Pros: Additional cell states enable to save more information of past sequences
  Cons: Complex structure results more computational cost
Gated Recurrent Unit (GRU)
  Computationally less expensive
  Better performance for less complex data
Recurrent Neural Network
Gated Recurrent Unit
Long Short Term Memory

## Slide 6: DL Approaches for Prediction
6/21
GAN (Generative Adversarial Network)
  Various usage
    Data generating model
    Classification model
    Prediction model

## Slide 7: DL Approaches for Prediction
7/21
LSTM
GAN
Usually used for prediction
Large amount of data is required for training
Former study achieved 91% of accuracy
Useful feedback from its adversaries
Trained to reflect whole distribution of data
Various types of data are available

## Slide 8: MoGAN
8/21
Data preprocessing
  Movement history (Sequence of PoA)
    Suppose the actual length of sequence is 5
    Movement history with less than 5 PoAs: ignored
    Movement history with more than 5 PoAs: divided
  For each PoA Transform into One-hot vector
    N-dimensional vector if there are total N points in the data

## Slide 9: MoGAN
9/21
Architecture
  Model for predicting next PoA of mobile devices
  Learns from the data consisting of previous sequences
Generator
Discriminator
Learns the distribution of previous PoA connections
Generates probable next PoA
Used as prediction model after training completed
Classifies between real PoA sequences and generated ones
Useful feedback for generator

## Slide 10: MoGAN
10/21

## Slide 11: MoGAN
11/21
Structure of generator

## Slide 12: MoGAN
12/21
Structure of discriminator
  For classification, FC layer performs better than RNN based structures
    For recognizing all the properties of structures

## Slide 13: MoGAN
13/21
Training procedure of MoGAN
  Error function: Binary cross entropy
    : Expected value, : Predicted value
  Step 1 (Minimax step)
  Step 2 (Additional training step for generator)

## Slide 14: MoGAN
14/21
Algorithm: The training procedure of MoGAN
Initialize: Number of total epoch , number of Step 2 per epoch , randomly initialized weights for Input:
1. Error function binary cross entropy 2. for do: 3. predicts next PoA 4. Combine with 5. D_loss_real Get loss value from D for real data 6. D_loss_fake Get loss value from D for generated data 7. Update to maximize D_loss_real + D_loss_fake Continue…
Algorithm: The training procedure of MoGAN

## Slide 15: MoGAN
15/21
Algorithm: The training procedure of MoGAN
Initialize: Number of total epoch , number of Step 2 per epoch , randomly initialized weights for Input:
8. G_loss_Step1 Get loss value from G for 9. Update to minimize G_loss_Step1 10. for do: 11. G_loss_Step2 Get loss value from G for 12. Update to minimize G_loss_Step2
Algorithm: The training procedure of MoGAN

## Slide 16: Evaluations
16/21
CMD (Campus Mobility Dataset)
  Collected from the wireless network of intelligent ICT Convergence Research Center in Pangyo, Republic of Korea
  12 APs, 289 users
AP#01
AP#02
AP#03
AP#04
AP#05
AP#06
AP#07
AP#08
AP#09
AP#10
AP#11
AP#12
Configuration
  Generator : GRU (512 nodes) + Output layer (12 nodes, softmax)
  Discriminator : FC (128 nodes, tanh) + FC (64 nodes, tanh) + Output layer (1 node, sigmoid)
  Adam optimizer (lr=0.001), 4000 epochs, 31 sequence lengths,
  Data Training : Test = 7 : 3

## Slide 17: Evaluations
17/21
Next PoA prediction accuracy comparison between MoGAN and vanilla GAN for different sequence lengths

## Slide 18: Evaluations
18/21
Analysis of MoGAN with different iterations of Step 2 training (𝛼) with increasing sequence length

## Slide 19: Evaluations
19/21
Performance comparison between MoGAN and stacked LSTM in terms of next PoA prediction accuracy and time cost

## Slide 20: Evaluations
20/21
MoGAN and LSTM performance comparison with limited data

## Slide 21: Conclusions
21/21
MoGAN achieved maximum 96.33% accuracy
  For perspective this means that if 3,000 users perform handover at a given time, MoGAN correctly predicts next PoA for 2,890 users
  Predicting next PoA for a user takes 5.85ms, which makes MoGAN suitable to be used in real mobile network
Improved method for data-based prediction is suggested which can be used in other domains
Future work
  Improvement of MoGAN through other attention mechanisms
  Extend MoGAN from single step to multiple step prediction

## Slide 22
Thank You!